OpenCPI Embedded
Installation Guide

DRAFT

Revision History
Revision	Description of Change	Date
1.0	Creation	2014-06-23
1.01	Add all FPGA and embedded system (Zed) content	2014-07-07
1.02	Update details for CentOS6 and Zed	2015-01-31
1.03	Update new simplified ZedBoard Installation	2015-02-27
1.1	Update for RPMs	2016-02-26

# References
This document assumes a basic understanding of the Linux command line (or “shell”) environment. It does not require a working knowledge of OpenCPI, although if anything goes wrong with the installation, more experience with OpenCPI may be required. The reference below is an overview of OpenCPI and may prove useful.

Title	Published By	Link
OpenCPI Technical Summary	OpenCPI	Public URL: https://github.com/opencpi/opencpi/raw/master/doc/OpenCPI_Technical_Summary.pdf

# Overview
This document describes how to install OpenCPI on an embedded platform. This guide expects that the development “host” has already been installed, see OpenCPI Installation for more details.
Preference is given to cross-building for embedded CPUs when possible, rather than self-hosting development tools on such platforms, in order to limit the complexities of installing tools on different development hosts. Additional installation options exist for other target processors and technologies such as various PCIe based FPGAs.
This document is focused only on the following class of target platforms:
Embedded CPUs
# Preparing a SD Card
The embedded targets in this document utilize a SD card for data storage and/or booting. The following section describes how to prepare a SD card for use as the OS boot and storage.
#### Preparing the SD Card
Before running setting up the SD card the device name of the SD card needs to be found. Start by ensuring the SD card is not present in the system. Open up a terminal and run the command:
% ls /dev/ > ~/before_card.txt
Insert the SD card and execute the following in the terminal:
% ls /dev/ > ~/after_card.txt
% diff ~/before_card.txt ~/after_card.txt
This command will provide the device name of the SD card. It will take the form of either /dev/mmcblk# or /dev/sd* depending on the host hardware configuration.
Insure that the SD card has been unmounted from the host system by running:
% mount | grep /dev/mmcblk#
or depending on the hardware configuration and the results from above.
% mount | grep /dev/sdX
to unmount any partitions run the following command while changing the muont point in the command to suit your enviroment:
% umount /run/media/my/mount/point
Format the SD card with the command:
% sudo /opt/opencpi/cdk/platforms/zed/formatSD.sh /dev/mmcblk#
or depending on the hardware configuration and the results from above.
% sudo /opt/opencpi/cdk/platforms/zed/formatSD.sh /dev/sdX
The results of the script will be the creation of two different partitions on the SD card, a 200MB partition named BOOT and a second partition of the remaining space. For verification run the following commands:
% ls /dev/mmcblk*
or depending on the hardware configuration and the results from above.
% ls /dev/sdX*

#### Manually Mounting the SD card
Once the SD card is formatted the card must be mounted. Depending on if the SD card has been ejected and reinserted it may be necessary to manually mount the partitions. In the following example it is assumed it is necessary to mount the drive and the mount point in /media/Boot.
To create the mount point execute the following command:
% sudo mkdir /run/media/user-name/BOOT
To mount the drive assuming the mmcblk* naming convention:
% sudo mount /dev/mmcblk#p0 /run/media/user-name/BOOT
or to mount the drive assuming the sdX naming convention:
% sudo mount /dev/sdX1 /run/media/user-name/BOOT
The SD card is now mounted and ready for use in the following sections.
# The Digilent ZedBoard with Xilinx Zynq SoC processor
Currently, the ZedBoard hardware platform is the smallest and least expensive example platform that supports OpenCPI driven software and FPGA development.
The steps outlined below describe the process of building OpenCPI and preparing a bootable SD card from scratch. This process includes assets from a Xilinx Linux kernel release as well as those built in OpenCPI.
For a quick start there is a prebuild SD card provided that allows the user to bypass step 4.2 In the OpenCPI code base, opencpi/platforms/zed/release, there is a prebuilt SD card directory. This directory contains all needed software for the ZedBoard in order to boot and utilize OpenCPI. The recommended SD card can be < 1GB.

## Quick start with reference ZedBoard SD Card image
The following set of instructions assumes the Host system has a RPM install completed. Any commands referenced below assume the SD card has been prepared as outlined in section 3.
### Copying files to the SD card
Assuming the SD card (first partition usually entitled “BOOT”) is mounted on /run/media/user-name, the following commands will remove its current contents and copy the OpenCPI contents onto it and unmount it as to be removed and plugged it into a ZedBoard.
% sudo rm -r -f /run/media/user-name/BOOT/*
% sudo cp -r -p platforms/zed/release/OpenCPI-SD/* /run/media/user-name/BOOT
% sudo umount /run/media/user-name/linux
% sudo umount /run/media/user-name/BOOT
For all options the user needs to enable console access to the ZedBoard, as described in the section below.
After removing the SD card, plug it into a properly configured (powered off) ZedBoard. Once powered on the board is ready to run pre-loaded simple applications. Section 4.2 discusses the steps necessary to customize the SD card.
## Establishing the Cross-Building Environment for OpenCPI targeting Zynq
This section describes how to build OpenCPI for the ZedBoard and enable building applications and components for the platform. This is the first step before executing or interfacing with the ZedBoard hardware. The basic steps are summarized at the end of this section.
### Install Xilinx ISE and EDK tools
There are two aspects to building for Zynq: user mode code and kernel driver code. Both rely on the cross-compiler supplied in the Xilinx tools release (the EDK). Thus the first prerequisite is to install Xilinx ISE and EDK tools. Therefore the current release would be installed in the
/opt/Xilinx/14.7
directory. This procedure has not been tested on ISE releases prior to 14.X. Be sure to choose an edition that includes the EDK (when running the Xilinx installer) as OpenCPI will use the cross compiler and some other required files. Currently OpenCPI does not support the Xilinx Vivado tools, only ISE and EDK.
As per the host installation document it is assumed that the Xilinx ISE+EDK installation occurs on CentOS6 64-bit or CentOS7 64-bit Linux.
The prerequisites for using OpenCPI on the ZedBoard (and other Zynq-based platforms) are:
1. A RPM installed framework for CentOS6 64-bit or CentOS7 64-bit Linux.
2. A Xilinx ISE+EDK installation at /opt/Xilinx/14.7
#### Establish and Customize the Cross Build Environment
To build OpenCPI for the Zynq platform, that utilizes the ARM processor architecture, the frame work uses the Xilinx EDK supplied ARM cross-compilation tools (cross compiling the executable and libraries from the host architecture to ARM). There is nothing specific to the ZedBoard platform about these cross-compilation tools.
% export OCPI_CROSS_HOST=arm-xilinx-linux-gnueabi
This command needs to be run in any terminal that is expected to build software components for zynq and not x86.
### Build FPGA libraries, components, platform and bitstreams
In order to build the HDL/FPGA code, including test bitstreams it is necessary to execute the following commands in the base project directory:
% cd hdl
% make hdl HdlPlatforms=zed
This will build all the primitive libraries, components, bitstreams for ZedBoard's Zynq SoC. If OpenCPI HDL/FPGA assets have already been built for zed the artifacts will not be rebuilt.
## Creating and Populating a Directory to Create a Bootable SD Card
The final software step to perform on the development system is to create and populate a directory to be copied to an SD card that can be plugged into the ZedBoard for booting. The contents of the SD card directory tree are a combination of:
- Binary files from a Xilinx Linux Kernel release from http://www.wiki.xilinx.com/Zynq+Releases
- Binary files built and stored in the OpenCPI tree that were patched from the Xilinx release and Linux source code.
- Core files from the OpenCPI tree built from sources.
- Component library files from the OpenCPI tree (RCC and HDL).
This resulting SD card can be used standalone (independent of the network) or require a network mounted files system. The network-based development setup mounts the development system from the ZedBoard using NFS, thus very few files are added to the SD card. In standalone mode, OpenCPI is expecting all the files on the SD card and with no requirement for network connectivity.
The OpenCPI release provides a pre-built populated SD card tree located at opt/opencpi/cdk/platforms/zed/release/OpenCPI-SD, that can be used directly. A directory tree is prepared by the RPM install and can be copied to a SD card. The resulting SD card can then be unmounted, plugged into the Zed board, and used to boot the ZedBoard.
There are two files that must be customized before making the SD card. One for standalone mode and one for network mode (NFS mounting of the development system). Please follow the appropriate section for the desired mode.
### Standalone mode start up script
Begin by making a copy of the defaultsetup.sh file located in the /opt/opencpi/cdk/platforms/zed directory and called mysetup.sh. Next customize the following settings if the defaults do not fit your needs:
- The system to be used as a time server
- The current timezone.
In CentOS, the following command will print what the timezone is set to:
% tail -1 /etc/localtime
The commands in the script configure the ZedBoard system for OpenCPI each time it boots. The ZedBoard does not have a real time clock and depends on the time server specified to set the time at each boot. If there is no network connection, the time server needs to be set to "-" and the time needs to be set manually when the ZedBoard boots. There is nothing in the OpenCPI framework that requires time to be set accurately but the time stamps on files created and edited would be wrong if this is not set.
The script will be copied on to the SD card, and it needs to be executed each time the system boots.
% cd /opt/opencpi/cdk/platforms/zed/
% cp defaultsetup.sh mysetup.sh
{ customize mysetup.sh }
#### Enable NFS on the Development Host for the "share" that includes OpenCPI
It is recommended but not required to export a mountable directory of the CDK and any built projects (i.e. base project and ocpiassets). If you want to run in standalone mode skip to section 4.3.3.
On CentOS6, enable NFS using :
% sudo yum install nfs-utils nfs-utils-lib
% sudo chkconfig nfs on
% sudo service rpcbind start
% sudo service nfs start
Add the following lines to the bottom of the /etc/exports file
% sudo vi /etc/exports

/opt/opencpi XX.XX.XX.XX(rw,sync,no_root_squash, no_subtree_check)

% sudo exports -a
Restart the services that have modified for the changes to take effect.
% sudo systemctl enable rpcbind
% sudo systemctl enable nfs-server
% sudo systemctl enable nfs-lock
% sudo systemctl enable nfs-idmap
% sudo systemctl restart rpcbind
% sudo systemctl restart nfs-server
% sudo systemctl restart nfs-lock
   % sudo systemctl restart nfs-idmap
For CentOS7 enabling NFS requires the following steps:
% sudo yum install nfs-utils nfs-utils-lib
-- Allow NFS past SELINUX
% sudo setsebool -P nfs_export_all_rw 1
% sudo setsebool -P use_nfs_home_dirs 1
-- Allow NFS past the firewall
% sudo firewall-cmd --permanent --zone=public --add-service=nfs
% sudo firewall-cmd --permanent --zone=public --add-port=2049/udp
% sudo firewall-cmd --permanent --zone=public –-add-service=mountd
% sudo firewall-cmd –-permanent –-zone=public --add-service=rpc-bin
% sudo firewall-cmd –-reload

Define the export by creating a new file that has the extension exports. If it does not have that extension it will be ignored.
Add the following lines to the bottom of the file
% sudo vi /etc/exports.d/user_ocpi.exports

/opt/opencpi XX.XX.XX.XX(rw,sync,no_root_squash,crossmnt)

If the file system that you are mounting is xfs the each mount needs to have a unique fsid in the exports file.
Add the following lines to the bottom of the file
% sudo vi /etc/exports.d/user_ocpi.exports

   /opt/opencpi XX.XX.XX.XX(rw,sync,no_root_squash,crossmnt,fsid=33)

Restart the services that have modified for the changes to take effect.
% sudo systemctl enable rpcbind
% sudo systemctl enable nfs-server
% sudo systemctl enable nfs-lock
% sudo systemctl enable nfs-idmap
% sudo systemctl restart rpcbind
% sudo systemctl restart nfs-server
% sudo systemctl restart nfs-lock
% sudo systemctl restart nfs-idmap
### Network mode startup script
Network mode is when development system hosts the OpenCPI tree as an NFS server to the ZedBoard as an NFS client. This configuration provides easy and dynamic access to all of OpenCPI, and presumably any components and applications.
The following settings on line 21 of the script will need to be modified:
- The directory that is being shared from the host. Defaulted to “/Users/jek/Business”. Its likely this should be changed to “/opt/opencpi”
- The directory name relative to that mountable file system where the OpenCPI tree lives. Defaulted to “ocpi/main/opencpi/ocpi”. Its likely that this should be changed to “cdk”
- The system to be used as a time server. Defaulted to “time.nist.gov”
- The current timezone description. Defaulted to “EST5EDT,M3.2.0,M11.1.0”
At boot the mynetsetup.sh runs the zednetsetup.sh script, which configures the ZedBoard system for OpenCPI each time it boots with support for network/NFS mode. The network address of the development system will be specified later, dynamically, as an argument to mynetsetup.sh.
% cd /opt/opencpi/cdk/platforms/zed/
% cp defaultnetsetup.sh mynetsetup.sh
{ customize mynetsetup.sh }
Note the "mynetsetup.sh" script copied to the SD card takes the development system's IP address as an argument. If it is fixed, the address can be prewritten in the script.
### Create new SD card contents directory
% sudo rm -r -f /run/media/user-name/BOOT/*
% sudo cp -r -p /opt/opencpi/cdk/platforms/zed/release/OpenCPI-SD/* /run/media/user-name/BOOT
% sudo cp -r -p mynetsetup.sh /run/media/user-name/BOOT/opencpi
% sudo cp -r -p mysetup.sh /run/media/user-name/BOOT/opencpi
% sudo umount /run/media/user-name/linux
% sudo umount /run/media/user-name/BOOT
At this point the development environment is ready for the ZedBoard. Everything has been built including libraries, executables, components, and examples for both software and FPGA, and have prepared a bootable SD card.
### Standalone SD card customization
The previous step created a universal SD image that contained the necessary files for both operational cases. In standalone mode all the necessary files that are needed must be included on the SD card. That requires the creation of new folder on the BOOT partition named artifacts.
% mkdir /mount/location/BOOT/opencpi/artifacts
Copy the contents of the components directory and any built assemblies that are needed into this folder.
### Summary of Pre-Hardware Steps to Prepare to Run OpenCPI on a ZedBoard
On a system that has a RPM install and a Xilinx ISE+EDK installation, in a fresh/new shell/window, do these steps:
% export OCPI_CROSS_HOST=arm-xilinx-linux-gnueabi
% make hdl HdlPlatforms=zed
% cp defaultsetup.sh mysetup.sh
% cp defaultnetsetup.sh mynetsetup.sh
{ customize mysetup.sh and mynetsetup.sh for the environment, etc. }
% sudo rm -r -f /run/media/user-name/BOOT/*
% sudo cp -r -p /opt/opencpi/cdk/platforms/zed/release/OpenCPI-SD/* /run/media/user-name/BOOT
% sudo cp -r -p mynetsetup.sh /run/media/user-name/BOOT/opencpi
% sudo cp -r -p mysetup.sh /run/media/user-name/BOOT/opencpi
% sudo umount /run/media/user-name/linux
% sudo umount /run/media/user-name/BOOT
Now everything is built and ready for the ZedBoard, and a bootable SD card has been created for using OpenCPI on a ZedBoard. The next section describes how to install the hardware and set it up to execute based on the OpenCPI system just built. There are two usage modes, one is network-based, where the ZedBoard can talk to the development (CentOS6/7) system via network and NFS, and the other is standalone/embedded mode where OpenCPI can be used even without a network connection.
Now everything is built and ready for the ZedBoard: a bootable SD card for using OpenCPI on a ZedBoard.
## Setting up the ZedBoard Hardware to Run OpenCPI
This section describes how, after installing Xilinx tools, installing and building OpenCPI (software and FPGA aspects) for Zedboard, and preparing an SD card, how to setup the ZedBoard to run OpenCPI applications and components.
These steps do not enable any particular devices that might be attached to the FPGA/PL part of Zynq.
Always be careful of static electricity when touching the board. Use Proper ESD procedures when touching the board.
### Set up the hardware jumpers and switches
It is recommended to have the Digilent ZedBoard Hardware Users Guide open for reference. This guide can be located at:
http://zedboard.org/sites/default/files/documentations/ZedBoard_HW_UG_v2_2.pdf
The “Jumpers” section, page 35, has a good photograph showing the location of jumpers on the board, reproduced here:
Only change the jumpers when the board is powered OFF. These are the required jumper settings:
- MIO 2:	set to GND : JP11
- MIO 3:	set to GND : JP10
- MIO 4:	set to 3V3 : JP09
- MIO 5:	set to 3V3 : JP08
- MIO 6:	set to GND : JP07
- J18:	VADJ Set to 1.8V (the setting is labeled 1V8)
- JP6:	shorted
- JP2:	shorted (needed to power USB peripherals or dongles).JP2:	shorted
All other jumpers should be left open. The power switch should be off.
### Insert the SD Card into the Socket on the Bottom of the Board.
Notice that the SD card is plugged in with its label down since that connector socket is on the back of the board.
### Connect the Supplied Micro-USB-to-normal-USB-cable to a System
This cable is what provides access to the ZedBoard's serial console. This is J14, the USB Micro B connector, located to the right of RJ45 Ethernet connector and labled UART. It must be connected to a system with a terminal emulator. Under Linux it is recommend to use screen with the following settings: 115200 baurd, 8 data bits, 1 stop bit, no parity. There are three different USB Micro B connectors on the board: be sure to use the one labeled: UART, and not the one labeled USB OTG, or PROG.
#### Apply Power to the ZedBoard
With the power supply cable connected, turn the power switch on. The green POWER LED should come on. The system has actually booted itself, but without a console attached the boot messages will not be seen.
### Get Access to the Serial Console of the ZedBoard, and Reboot from There
Since the OpenCPI development environment is running on a Linux system, the USB cable can be directly plugged into the system, and it will automatically create a "/dev/ttyXXX" file for this connection. Typically the file name is /dev/ttyACM0, but not always.
There are many alternative terminal emulation applications to provide for this USB remote serial console for the ZedBoard. One that is available in the standard CentOS repository is "screen", obtainable by issuing the following command:
% sudo yum install screen
Then in any terminal window, enter:
% sudo screen /dev/ttyACM0 115200
To exit this program, use the sequence: Control-a followed by backslash.
With the terminal emulator connection running, hit return a few times in the serial console window to see the "zynq login:" prompt, or, if the system was previously logged in and running, it might appear as "root@zynq:~#" prompt. Login as "root" with the password "root".
Sometimes if the screen or terminal emulator is confused, or if, after hitting "return", the prompt stays on the same line, try typing the command "clear", to clear the state of the terminal emulator.
The user may wish to use SSH to login to the zedboard and leave the console window alone. After the board boots, log in with SSH without using the console at all if the DHCP network address is known. The "ifconfig" command on the zed will print the internet address.
The user can now log in (root, root), and see that rebooting works fine by both trying the "reboot" command, as well as pressing the reset button on the board (labeled: PS_RST).
Linux booting has been verified, and console and ssh access is enabled.
### Get the Network Working to Talk to the Development System
Standalone mode developers, without needing a network or connection to the development host, should skip to Standalone Mode section below.
To enable the network connection to the development host, connect the Ethernet connector on the ZedBoard to a LAN with DHCP. The green light that is part of the network connector socket should come on to indicate that there is a network connection.
After reboot, and login use the ifconfig command to confirm that the "eth0" interface (or "eth1" for USB Ethernet dongles) has an internet address.
root@zynq:~# ifconfig
eth0 Link encap:Ethernet HWaddr 00:0A:35:00:01:22
     inet addr:10.0.1.108 Bcast:0.0.0.0 Mask:255.255.255.0
     inet6 addr: fe80::20a:35ff:fe00:122/64 Scope:Link
     UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
     RX packets:42 errors:0 dropped:1 overruns:0 frame:0
     TX packets:14 errors:0 dropped:0 overruns:0 carrier:0
     collisions:0 txqueuelen:1000
     RX bytes:6793 (6.6 KiB) TX bytes:1737 (1.6 KiB)
     Interrupt:54 Base address:0xb000
The network address is also printed out on the console during booting. To ensure connectivity, use ping, in both directions: ping the development host from the ZedBoard console and ping the ZedBoard from the development host.
### Run the Setup Scripts after Booting to Access the Development System
When Linux boots on the ZedBoard from the SD card created as above, it creates a memory-based root file system, initialized from decompressing the uramdisk.image.gz file on the SD card. It also mounts the SD card itself as a file system, at /mnt/card. This means that anything written to the root file system is not persistent and is lost on a reboot. To create or edit any files the SD file system must be used, which is located at /mnt/card.
### Networked mode
The network setup uses the built-in NFS client to access the OpenCPI code base from the host development environment.
After booting, and logging in as root (either via the serial console or ssh), source the start-up script on the SD card, supplying the development host's IP address as an argument.
root@zynq:~# source /mnt/card/opencpi/mynetsetup.sh 10.0.1.108
This command, executed once per boot (not per ssh login), are all that is necessary to enable OpenCPI.
### Standalone mode
To run in standalone mode, which has no requirement of a network, but can use one if present, after booting execute the following command:
# source /mnt/card/opencpi/mysetup.sh
This will set up the environment to run some applications locally based on files in the SD card, without accessing any files on the network.
The opencpi subdirectory on the SD card has executables and scripts in the "bin" directory, component artifacts in the "artifacts" directory, and xml applications in the "xml" directory.
The steps to run OpenCPI applications without and with FPGA components are in the previous two sections and work in standalone mode as well as network mode.
### Confirm OpenCPI Software Operation.
Both the standalone and network scripts set the path to find OpenCPI executables and software components. It may also change to a known working directory. The default setup script (that was modified), changes to this directory. In standalone mode, the script changes to the /mnt/card/opencpi/xml directory.
To run a simple test application:
zynq> ocpirun -v -d -mbias=rcc testbias
This should run the testbias application (using file_read->bias->file_write) components, running as software components.
### Confirm OpenCPI Execution of an FPGA-based application
There is no bitstream loaded on power up on the ZedBoard, but one will be loaded automatically as needed. Assuming the OCPI_LIBRARY_PATH points to the built-in bitstream (which the default setup file do in both network and standalone mode), you can run:
zynq> ocpirun -v -d -mbias=hdl testbias
which runs the same application with the bias component on the FPGA, with the appropriate bitstream being automatically loaded.

# Appendix-A Embedded Systems as Target Hosts
In this document the term “embedded systems” is used for processors and systems that execute OpenCPI components and applications, but are not used to build or compile OpenCPI or components. The primary example is the Digilent ZedBoard, which has a Xilinx Zynq SoC chip which contains 2 ARM cores for software and FPGA fabric.
When using any embedded system, the first step is to install the appropriate cross-compilation tools on the development system. While some embedded systems can actually host their own tools, it is generally recommended to avoid this for two reasons. First, to discourage burdening the embedded platform with such tools, and second to avoid the challenges associated with porting the OpenCPI development environment to a new platform.
If no Linux-hosted cross-tools are available for the embedded target, then the OpenCPI build/development environment is required to be ported to that platform. The OpenCPI development environment does not have many dependencies, but those that do exist must be addressed on the new development platform. This is a partial list of dependencies that some aspects of the OpenCPI development environment require:
- C and C++ compilers and linkers
- Google test
- XZ compression Utility
- Bash and Make
- Python
- Miscellaneous POSIX utilities such as “tr”, “sed”, “cp”, etc.
Along with using cross-compilers it is assumed (in a development context) that the embedded system has a network interface. The network interface enables the embedded platform to mount and access the file systems of the development system. Here the host provides access to the OpenCPI code base and artifacts. The host system will need to be enabled as a file server. Any associated firewall issues need to be addressed between the embedded system and the development host.
When network access to the development system is not desired, then a small subset of the OpenCPI cross-built environment is copied to the embedded system. In this mode a system is refereed to as “standalone” or “embedded” mode.
For each embedded system that is supported, the instructions are divided into the follow steps:
1. Install cross development tools and cross-build OpenCPI on the development system.
2. Create a boot-able kit (usually an SD card) to install on the embedded system, using the development system.
3. Set up the hardware as needed for OpenCPI.
4. Install the boot-able kit (usually plugging in an SD card) on the embedded system.